## Slide 1: Soil Mechanics
Instructor:
M.M.Ahmadi

## Slide 2: Seepage
Chapter 8

## Slide 3: Seepage
Laplace’s Equation of Continuity
Continuity Equation for Solution of Simple Flow Problems
Flow Nets
Seepage Calculation from a Flow Net
Flow Nets in Anisotropic Soil
Mathematical Solution for Seepage
Uplift Pressure Under Hydraulic Structures
Seepage Through an Earth Dam on an Impervious Base
L. Casagrande’s Solution for SeepageThrough an Earth Dam
Filter Design

## Slide 4: Calculation of Head
Bernoulli's Equation
For Seepage through soil:
Pore Water Pressure (kPa)
Piezometric head (m)

## Slide 5: Calculation of Head
Total Head Loss, h in water seeping from A to B:
hA
A
B

datum
zA
hB
zB
h
hydraulic grade line
L
Hydraulic Gradient (Slope), i:
In terms of Bernouli:

## Slide 6: Laplace’s Equation of Continuity

## Slide 7: Laplace’s Equation of Continuity

## Slide 8: Laplace’s Equation of Continuity
Assuming that water is incompressible and that no volume change in the soil mass occurs, we know that the total rate of inflow should equal the total rate of outflow. Thus:

## Slide 9: Laplace’s Equation of Continuity
According to Darcy’s law:
So we can write :
For isotropic soil: kx= kz

## Slide 10: Solutions for Laplace’s Equation of Continuity
Analytical Solution
Finite Element
Finite Difference
Electrical Analogy
Flow Net

## Slide 11: Flow Nets

## Slide 12: Flow Nets
The equation for flow nets originates from Darcy’s Law.
Flow Net solution is equivalent to solving the governing equations of flow for a uniform isotropic aquifer with well-defined boundary conditions.

## Slide 13: Flow Nets
The continuity equation in an isotropic medium represents two orthogonal families of curves—that is, the flow lines and the equipotential lines.
A flow line is a line along which a water particle will travel from upstream to the downstream side.
An equipotential line is a line along which the potential head at all points is equal.
A combination of a number of flow lines and equipotential lines is called a flow net.

## Slide 14: Flow Nets
Flow nets are constructed for the calculation of groundwater flow and the evaluation of heads in the media.
To complete the graphic construction of a flow net :
1. The equipotential lines intersect the flow lines at right angles.
2. The flow elements formed are approximate squares.

## Slide 15: Flow Nets under a sheet pile
Nf = the number of flow channels in the flow net
Nd = the number of potential drops

## Slide 16: Flow Nets
For the flow net under sheet pile, the following four boundary conditions apply:
Condition 1: The upstream and downstream surfaces of the permeable layer (lines ab and de) are equipotential lines.
Condition 2: Because ab and de are equipotential lines, all the flow lines intersect them at right angles.
Condition 3: The boundary of the impervious layer—that is, line fg—is a flow line, and so is the surface of the impervious sheet pile, line acd.
Condition 4: The equipotential lines intersect acd and fg lines at right angles.

## Slide 17
Flow Nets under a sheet pile

## Slide 18: Flow Nets under a dam with toe filter

## Slide 19
1. Draw Flow Channel Boundaries
19
2. Draw Equipotential Boundaries
To construct a flow net, you must start with a scale drawing of the hydraulic structure:
Upstream Equipotential Boundary
Downstream Equipotential Boundary

## Slide 20: Drawing Flow Nets
h = h
half way mark
x
y
z
h = 0.5h
h = 0
If we divide the seepage journey into equally spaced drops in head then we get a flow net.

## Slide 21
bedrock
sand
Flow Nets under a sheet pile

## Slide 22
bedrock
sand
Flow Nets under a sheet pile

## Slide 23
bedrock
sand
Flow Nets under a sheet pile

## Slide 24
bedrock
sand
Flow Nets under a sheet pile

## Slide 25
soild
Reservoir
Tail water
bedrock
Flow Nets under dam

## Slide 26
soild
Reservoir
Tail water
bedrock
Flow Nets under dam

## Slide 27
Reservoir
Tail water
bedrock
soil
Flow Nets under dam

## Slide 28
Reservoir
bedeock
soil
Flow Nets under dam

## Slide 29
Reservoir
bedeock
soil
Flow Nets under dam

## Slide 30
Reservoir
bedrock
soil
Flow Nets under dam

## Slide 31: Seepage Calculation from a Flow Net
In any flow net, the strip between any two adjacent flow lines is called a flow channel.

## Slide 32: Seepage Calculation from a Flow Net
From Darcy’s law :
Thus,
And
)=
where H =head difference between the upstream and downstream sides
Nd =number of potential drops

## Slide 33: Seepage Calculation from a Flow Net
If the number of flow channels in a flow net is equal to Nf, the total rate of flow through all the channels per unit length can be given by :
Although drawing square elements for a flow net is convenient, it is not always necessary. Alternatively, one can draw a rectangular mesh for a flow channel, provided that the width-to-length ratios for all the rectangular elements in the flow net are the same

## Slide 34: Seepage Calculation from a Flow Net
In this case,

## Slide 35: Head drop in flow net

## Slide 36: Pressure head at any point
Total head=hL - numbers of drops from upstream x h
Elevation head = z (-ve number in this figure)
Pressure head = Total head – Elevation head

## Slide 37
Example 1: A flow net for flow around a single row of sheet piles in a permeable soil layer is shown in the figure next page. Given that kx = kz = k = cm/s, determine:
How high (above the ground surface) the water will rise if piezometers are placed at points a and b
The total rate of seepage through the permeable layer per unit length
The approximate average hydraulic gradient at c
Seepage Calculation from a Flow Net

## Slide 38
Example 1
Seepage Calculation from a Flow Net

## Slide 39
Part a :
we have Nd = 6, H1 = 5.6 m, and H2 = 2.2 m. So the head loss of each potential drop is :
Seepage Calculation from a Flow Net
At point a, we have gone through one potential drop. So the water in the piezometer will rise to an elevation of (5.6 - 0.5672) = 5.033 m above the ground surface
At point b, we have five potential drops. So the water in the piezometer will rise to an elevation of (5.6-5(0.567))= 2.765 m above the ground surface

## Slide 40
Part b :
Flow channel 3 has rectangular elements. These elements have a width-to-length ratio of about 0.38; hence,
So, the total rate of seepage can be given as:
Seepage Calculation from a Flow Net

## Slide 41
Part c : The average hydraulic gradient at c can be given as :
Seepage Calculation from a Flow Net

## Slide 42
Multiple choice question 1:If k = 10-7 m/s, what would be the flow per day over a 100 m length of wall?
A. 7 m3/day
B. 14 m3/day
C. 28 m3/day
D. 35 m3/day

## Slide 43
solution:
Nf = 5
Nd = 14
h = 45 m
k = 10-7 m/s
q = 10-7(5/14) 45 x 100 m length
q = 0.000161 m3/s
q = 13.9 m3/day

## Slide 44
Multiple choice question 2: According to this figure, which one of these choices is correct?
A. hX = hY > hW
B. hX > hY > hW
C. hX = hW > hY
D. hX > hW > hY
Solution:
X & W are located in the same equipotential line (cf Line)
hX = hW
Head at cf Line = H-2Δh
Head at cg Line = H-4Δh
hX > hY

## Slide 45
Multiple choice question 3: According to this figure, which one of these choices is correct?
A. uX = uY
B. uX < uY
C. uX = uW
D. uX < uW
Solution:
Consider MN Line as Datum

## Slide 46
Multiple choice question 4: According to this figure, if MN Line is considered as datum, H1=4m and H2=1m, the pressure head at point X is:
A. 3.0m B. 4.5m
C. 5.5m D. 6.0m
Solution

## Slide 47: Flow Nets in Anisotropic Soil
Step 1: Adopt a vertical scale (that is, z axis) for drawing the cross section.
Step 2: Adopt a horizontal scale (that is, x axis) such that :
vertical scale.
Step 3: With scales adopted as in Steps 1 and 2, plot the vertical section through the permeable layer parallel to the direction of flow.
Step 4: Draw the flow net for the permeable layer on the section obtained from Step 3, with flow lines intersecting equipotential lines at right angles and the elements as approximate squares.
horizontal scale =

## Slide 48: Flow Nets in Anisotropic Soil
A flow element in anisotropic soil:
(a) in transformed section;
(b) in true section

## Slide 49: Flow Nets in Anisotropic Soil
Example 2: A dam section is shown in the figure below . The hydraulic conductivity of the permeable layer in the vertical and horizontal directions are mm/s and mm/s, respectively. Draw a flow net and calculate the seepage loss of the dam.

## Slide 50
Flow Nets in Anisotropic Soil

## Slide 51
The rate of seepage is given by:
From Scaled Figure, Nd=8 and Nf = 2.5 (the lowermost flow channel has a width-to-length ratio of 0.5). So,
Flow Nets in Anisotropic Soil

## Slide 52: Mathematical Solution for Seepage
The seepage under several simple hydraulic structures can be solved mathematically. Harr (1962) has analyzed many such conditions.
The following graph shows a non-dimensional plot for the rate of seepage around a single row of sheet piles.

## Slide 53
Mathematical Solution for Seepage

## Slide 54
In a similar manner, the following graph is a non-dimensional plot for the rate of seepage under a dam. The depth of penetration of the sheet pile is S, and the thickness of the permeable soil layer is T.
Mathematical Solution for Seepage

## Slide 55
Mathematical Solution for Seepage

## Slide 56: Mathematical Solution for Seepage
Example 3:
Given; the width of the dam, B =6 m; length of the dam, L =120 m; S =3 m; =6 m; x =2.4 m; and H1 - H2 = 5 m. If the hydraulic conductivity of the permeable layer is 0.008 cm/s, estimate the seepage under the dam (Q) in m3/day.

## Slide 57: Mathematical Solution for Seepage
Example 3:

## Slide 58: Mathematical Solution for Seepage

## Slide 59: Mathematical Solution for Seepage

## Slide 60: Heads at a Point X
impervious strata
concrete dam
datum
X
z
h
H = h
Total head = h - # of drops from upstream x h
h
Elevation head = z (-ve number in this figure)
Pressure head = Total head – Elevation head

## Slide 61: Uplift Pressure under Hydraulic Structures
The pressure distribution diagram at the base can be obtained from the equipotential lines as follows.
The head loss for
each potential drop is :
Uplift pressure at point a (left corner of the base) = (Pressure head at point a) ₓ (γw )
= [(7+2)-1] γw=8 γw

## Slide 62: Uplift Pressure Under Hydraulic Structures
Uplift pressure at point b = (Pressure head at point b) ₓ (γw ) = [9-2*1] γw=7 γw
Uplift pressure at point f = (Pressure head at point f) ₓ (γw ) = [9-6*1] γw=3 γw

## Slide 63
Multiple choice question 6: According to this figure, if h1=6m, H1=2m, H2=1m, k1=10-4cm/s and k2=5x10-5cm/s, the pressure head at AB Line (h2) is:
A. 4m B. 3m
C. 2m D. 1m
Solution

## Slide 64
Dam failure due to seepage

## Slide 65
Dam failure due to seepage

## Slide 66
Example of dam failure due to seepage: Baldwin Hills dam broke in 1963 due to seepage.

## Slide 67
Example of dam failure due to seepage: Baldwin Hills dam broke in 1963 due to seepage.

## Slide 68
Example of dam failure due to seepage: Baldwin Hills dam broke in 1963 due to seepage.

## Slide 69
Example of dam failure due to seepage: Baldwin Hills dam broke in 1963 due to seepage.

## Slide 70
Example of dam failure due to seepage: Fontenelle dam broke in 1965 due to seepage.

## Slide 71
Example of dam failure due to seepage: Around 7:00 am on June 5, 1976 a leak about 30 m from the top of Teton dam was observed.

## Slide 72
Example of dam failure due to seepage: Teton dam Dam broke at 11:59 AM

## Slide 73
Seepage Through an Earth Dam on an Impervious Base

## Slide 74
The slope of the free surface can be assumed to be equal to the hydraulic gradient . It is also assumed that this hydraulic gradient is constant with depth :
Considering the triangle cde :
So :
Seepage Through an Earth Dam on an Impervious Base

## Slide 75: Seepage Through an Earth Dam on an Impervious Base
Again, the rate of seepage (per unit length of the dam) through the section bf :
For continuous flow :
By integrating the following equation we have :

## Slide 76: Seepage Through an Earth Dam on an Impervious Base
By doing some mathematical calculation :
Step to find seepage rate :
Step 1: Obtain .
Step 2: Calculate and then
Step 3: Calculate d.
Step 4: With known values of and d, calculate L from Eq.2 .
Step 5: With known value of L, calculate q from Eq.1.

## Slide 77: Seepage Through an Earth Dam on an Impervious Base
Example 5 : Refer to the earth dam shown in the figure below. Given that , B = 3 m, H = 6 m, height of dam = 7.6 m, and k m/min, calculate the seepage rate, q.

## Slide 78: Seepage Through an Earth Dam on an Impervious Base

## Slide 79: L. Casagrande’s Solution for Seepage through an Earth Dam
Also a graphical solution was provided by
Gilboy (1934) :

## Slide 80: L. Casagrande’s Solution for Seepage through an Earth Dam
In order to use the graph :
Step 1: Determine d/H.
Step 2: For a given d/H and determine m.
Step 3: Calculate .
Step 4: Calculate .

## Slide 81: Drawing Flow Nets

## Slide 82
Multiple choice question 5: An atmospheric line is defined as a line within a dam section below which there are:
A. positive hydrostatic pressures
B. positive equipotential lines
C. negative hydrostatic pressures
D. negative equipotential lines

## Slide 83: Filter Design
For proper selection of the filter material, two conditions should be kept in mind:
Condition 1: The size of the voids in the filter material should be small enough to hold the larger particles of the protected material in place.
We call this condition, Retention Criteria.
Condition 2: The filter material should have a high hydraulic conductivity to prevent buildup of large seepage forces and hydrostatic pressures in the filters.
We call this condition Permeability Criteria.

## Slide 84: Filter Design
When seepage water flows from a soil with relatively fine grains into a coarser material, there is danger that the fine soil particles may wash away into the coarse material.
Over a period of time, this process may clog the void spaces in the coarser material. Hence, the grain-size distribution of the coarse material should be properly manipulated to avoid this situation.
granular filter
A properly designed coarser material is called a filter

## Slide 85: Filter Design
It can be shown that, if three perfect spheres have diameters greater than 6.5 times the diameter of a smaller sphere, the small sphere can move through the void spaces of the larger ones.

## Slide 86: Filter Design
If the pore spaces in a filter are small enough to hold D85 of the soil to be protected, then the finer soil particles also will be protected This means that the effective diameter of the pore spaces in the filter should be less than D85 of the soil to be protected.

## Slide 87: Filter Design
The effective pore diameter is about of the filter. With this in mind and based on the experimental investigation of filters, Terzaghi and Peck (1948) provided the following criteria to satisfy Condition 1:

## Slide 88: Filter Design
In order to satisfy Condition 2, they suggested that :

## Slide 89: Filter Design
The proper use of the equations to determine the grain-size distribution of soils used as filters is shown.

## Slide 90: Filter Design
The U.S. Navy (1971) requires the following conditions for the design of filters.
Condition 1: For avoiding the movement of the particles of the protected soil:

## Slide 91: Filter Design
Condition 2: For avoiding buildup of large seepage force in the filter:
Condition 3: The filter material should not have grain sizes greater than 76.2 mm (3 in.). (This is to avoid segregation of particles in the filter.)

## Slide 92: Filter Design
Condition 4: To avoid internal movement of fines in the filter, it should have no more than 5% passing a No. 200 sieve.
Condition 5: When perforated pipes are used for collecting seepage water, filters also are used around the pipes to protect the fine-grained soil from being washed into the pipes. To avoid the movement of the filter material into the drain-pipe perforations, the following additional conditions should be met:

## Slide 93: Summary of Filter Design
Retention criteria:
D15, filter < 5 D85, soil
Permeability criteria:
D15, filter > 4 D15, soil
average filter pore size
Terzaghi & Peck (1967)
D15, filter < 20 D15, soil
D50, filter < 25 D50, soil
US Navy (1971)

## Slide 94
Multiple choice question 7: Based on Terzaghi & Peck criteria for filter design, which one of these choices is correct?
A. D15,filter > D85,soil
B. D15,filter < D15,soil
C. D15,filter < 5D85,soil
D. D15,filter > 5D85,soil

## Slide 95
Multiple choice question 8: Based on Terzaghi & Peck criteria for filter design, For avoiding buildup of large seepage force in the filter we must have:
A. D15,filter > 4D15,soil
B. D15,filter > 4D85,soil
C. D15,filter < 4D15,soil
D. D15,filter < 4D85,soil